## Slide 1: Network Forensics
Switches, Routers, and Firewalls
Week 10
S. Pradono Suryodiningrat
satrio.Pradono@binus.ac.id

## Slide 2: Session Learning Outcomes
Upon completion of this session, students are expected to be able to
Identify different techniques of capturing digital evidence from a scene in network forensics, technology, and principles
Define appropriate tools necessary to sample, seal, and dissect a given intrusion evidence, and concept of network forensics and traffic analysis
Conduct laboratory experiments in network forensics and evidence handling

## Slide 3: Storage Media
ROM
NVRAM
DRAM
CAM
Hard Drive

## Slide 4: Switches
Maps MAC addresses to switch ports
Locate physical location of MACs
ARP tables

## Slide 5: CAM Tables
Very fast memory
Maps MAC Addresses to physical switch ports
    Switch looks up MAC in table
    Writes packet to the correct port
If an attacker is sniffing local traffice it will show up in the CAM table
The CAM table is very volatile

## Slide 6: CAM Table
“Age” is the number of seconds left before the entry expires.

## Slide 7: ARP Tables
MAC address to IP address resolution
Format of table entry
    Location of the ARP requeset
    IP Address
    MAC address
    Age in seconds from initial ARP request

## Slide 8: ARP Table
Arp table for a linux workstation
Cisco ASA 5505 firewall
Ubuntu Server

## Slide 9: Managed Switches
Enterprise LANS
    Support for VLAN, ACLs
    Arp caching, 802.1 authentication
    Port mirroring/monitoring
    Event logging
    Config Interfaces
      CLI, SSH/Telnet, SNMP, Web, Proprietary- Cisco
    Performance Monitoring

## Slide 10: Smart Switches
Subset of Managed Switches
    VLANs
    ARP caching
    Port mirroring
    Some performance monitoring
Config Interface
    Usually Web
    CLI and remote CLI

## Slide 11: Home Switches
Unmanaged Switches
    Plug and play
    No configuration interface
    No accessible stored data
    No/limited forensic value

## Slide 12: Switch Evidence
Volatile Data
    Stored packets ( prior to forwarding)
    CAM tables (MAC to port mappings)
    ARP Table (MAC to IP address mappings)
    ACLs, Running configuration
    Flow data and performance stats
Non-Volatile Data
    OS image and Startup configuration
Off-System
    Logging data
    Flow data

## Slide 13: Routers - Why?
Network topology
Traffic through the router
Logged data
    all routers are capable of extensive logging
The router itself may be compromised!
Types of Routers
    Enterprise
    Consumer
    Custom – Linux boxes

## Slide 14: Enterprise router
Extensive selection - $ - $$$$$
Capabilities
    Stateful packet filtering
    Supports many routing protocols
    Multiprotocol Label Switching
    High-availability, high-throughput
    DHCP, NAT QoS
    Performance monitoring
    Event logging

## Slide 15: Router Interfaces
Configuration Interfaces
    CLI, Telnet/SSH, SNMP
    Web interface
    Cisco Proprietary
    Central Management
      Cisco Works Management Center
Central management
    Central management of large numbers of touters
Cisco ASA seties
Juniper J-Series

## Slide 16: Consumer Grade Routers
Linksys, D-Link, ISP Custom
Often supplied by the ISP
    Caution!
Capabilities
    ISP connection via PPPoE
    DHCP, NAT
    802.11 wireless interface
    Port Filtering
    Easy config via Web interface
    Remote access to config

## Slide 17: Router Evidence Volatile
Routing Tables
Packet counts & stats
ARP table
DHCP lease assignments
ACLs
Running config
Flow data & stats
I/O and processor memory

## Slide 18: Router Evidence Non-Volatile
OS image
Boot loader
Stored configuration
Access logs
DHCP logs

## Slide 19: Router Evidence Remote
Configurable – via
    Syslog, FTP, TFTP, SNMP
Access history
DHCP logs
Backup configuration
Flow data

## Slide 20: Firewalls
Firewall logs include extensive info
    Connection attempts
      Success or failure
    Protocols used
    Applications
Configuration
    What does the world see
    Net topology
Configurable to collect more data
Firewall may be compromised

## Slide 21: Firewall Types
Packet Filters
    Iptables types
Session-Layer Proxies
    Source establishes connection with proxy
    Destination establishes connection with proxy
    Man in the middle intercept of SSL connections for deep packet inspection of encrypted traffic
Application Proxies
    Enables inspection of layer 7 traffic

## Slide 22: Enterprise-class Firewalls
Often higher layer proxies are often standalone devices
Firewall features/capabilities
    NAT, DHCP, VPN tunneling
    Load balancing
    Fail over
    Fragmentation reassembly
    Stateful filtering, performance monitoring
    Centralized management, Event logging
    HW upgrades

## Slide 23: Configuration Interfaces
CLI
Remote CLI via SSH/Telnet
SNMP
Web interface
Proprietary
Remote access = insecurity!

## Slide 24: Consumer Grade Firewalls
Provides
    NAT
    DHCP
    WiFi interface
    Some packet filtering
    Some logging

## Slide 25: Firewall Evidence
Volatile
    Similar to routers
    Command history
Persistent
    Boot load, startup config
    Access logs, DHCP logs
    Firewall rules and exceptions
    TURN IT ON
Remote
    Usual logs

## Slide 26: Interfaces
CLI
    Cisco ASA 5505 is typical

## Slide 27: Cisco ASA 5505 Continued

## Slide 28: Logging
Cisco ASA 5505

## Slide 29: Other Logs
Syslog, rsyslog, etc.
AAA logs
    Authentication
    Authorization
    Accounting
Files usage logs